## Slide 1: Simple Machines
Simple Machine- a tool with few parts that makes it easier or possible to do work.
6 common simple machines
  Lever
  Pulley
  Inclined Plane
  Wedge
  Screw
  Wheel and Axle

## Slide 2: Lever
Lever- a simple machine that makes it easier or possible to do work
Fulcrum- a fixed point around which a lever rotates.
Effort Force- The force applied to a machine by the user
Resistance Force- The force applied to a machine by the object to be moved

## Slide 3: 3 Classes of Levers
First- Class Lever
  The Fulcrum is between the Effort and the Resistance
  Changes the direction of the force
  Increases the force

## Slide 4: 2nd Class Lever
The Resistance is positioned between the Effort and the Fulcrum.
Always increased the force
Do NOT change the direction of the force
E.g. wheelbarrow

## Slide 5: 3rd Class Lever
The Effort force is between the Fulcrum and Resistance
Increases the distance through which the force moves, which causes the resistance to move farther and faster

## Slide 6: Work and Efficiency
Energy cannot be created or destroyed.
No simple machine can do more work than the person using it supplies.
It CAN increase or change the direction of the force.

## Slide 7: Work and Efficiency (cont.)
Work Input- work put into a machine by its user
Work Output- work done by a machine against the resistance
Efficiency- how well a machine performs
  Efficiency = work output X 100%
            work input

## Slide 8: Mechanical Advantage
People use simple machines to make work easier.
Mechanical Advantage- factor by which a machine multiplies the effort force.
  MA = Resistance Force
        Effort Force

## Slide 9: Mechanical Advantage (cont.)
Effort Arm- The distance between the fulcrum and the effort force of a lever.
Resistance arm- The distance between the fulcrum and the resistance force of a lever.
  MA = effort arm
      Resistance arm

## Slide 10: Pulley
Pulley- a simple machine made of a rope, chain, or belt wrapped around a wheel.
  Single fixed pulley – changes the direction of the force. MA= 1. Use this type of pulley to lift a heavy object by pulling down instead of lifting up.
  Fixed Pulley- is attached at the top. The wheel is free to spin, but it cannot move up or down
  Moveable Pulley- when effort is applied, the entire pulley and the object attached will rise.
  MA= 2. Needs only half the force to lift it.

## Slide 11: Pulley (cont.)
Pulley system-
Block and Tackle